## Slide 1: Secure Home Gateway project - Prototype development - IoT security focused - Idea & vision - challenges
Jacques Latour, CTO, CIRA Labs Canadian Internet Registration Authority Jacques.Latour [@] cira.ca September 2018

## Slide 2: Today's home network and IoT products and solutions lack secure testing and design. Home network require active monitoring to mitigate the risks of attack.
home network = home and small business network
Notes: http://www.istockphoto.com/ca/photo/internet-of-things-concept-with-network-of-connected-objects-gm644680544-116869175

## Slide 3: The home network of the future must be safe, private, secure and most of all easy to use.
The IETF HOMENET WG is making progress at making it easy to use
Notes: http://www.istockphoto.com/ca/photo/circular-futuristic-interface-of-smart-home-automation-assistant-virtual-screen-gm637770524-113940363

## Slide 4: The Home network must be reachable from the internet seamlessly and securely
IPv6 makes connectivity to the home seamless and visible We must make it secure
Notes: http://www.istockphoto.com/ca/photo/businessman-touching-a-cloud-connected-to-objects-internet-of-things-gm514785054-88267551

## Slide 5: The home network grows to include personal and wearable IoT, inside and outside the home…
Notes: http://www.istockphoto.com/ca/photo/man-wearing-vr-headset-gm583697902-99848893

## Slide 6: Your home network security both internal and external must be protected by using a simple and user friendly model. Typing passwords is a thing of the past.
Notes: http://www.istockphoto.com/ca/photo/smart-phone-remote-for-smart-home-hologram-technology-concept-gm839028202-137738281

## Slide 7: How did we get here?
Our assessment of the home network and IoT security posture post MIRAI attack clearly identified a need for additional home security measures to protect the internet from compromised IoT devices and a very strong need for an enhanced open source home security framework.
Our work so far has identified a significant gaps in open source projects to implement an enhanced home security framework
We embarked on a journey to identify these gaps and start development of many open source projects to better the internet 

## Slide 8: Secure Home Gateway (SHG) Primary Project Goal
The primary goal of this project is to develop a secure home gateway that;
  protects the internet from IoT devices attacks and
  protects home IoT devices from the internet attacks
x
x

## Slide 9: Scope of Work and Goals
We are developing an advanced security framework for small network (home and small business) gateways based on integrating existing and emerging technologies & standards
Goals:
  Develop a functional SHG prototype
  Develop a simple management interface to provision complex network
  Identify new standards requirements and updates
  To enhance small network privacy & security with ‘intent based’ network access controls
  To have open source running code & standards
  Develop a framework to provision SHG domain names

## Slide 10: Why are we working on this? -> Risk mitigation
For many internet organizations like CIRA the #1 risk on the risk register is a large scale (Dyn like) DDoS attack.
One of the mitigation mechanisms for this risk is to prevent ‘weaponization’ of IoT devices
Tightly controlling access ‘to’ and ‘from’ IoT devices inside the home or small office network is key to preventing ‘weaponization’ and causing harm on the internet.
The threat that IoT devices bring is the scale of attacks. The uncontrolled access of million/billions of IoT devices to and from the internet is the threat we need to mitigate.

## Slide 11: Overview of the IoT threat landscape -> Scale and capacity
IoT device compromises:
  Used in internet attacks i.e. MIRAI/DYN Attack (DDoS) targeting DNS servers (~1.2 Tbs)
IoT traffic generation, reflection and amplification
  IoT device used various attacks (DDoS) NTP, DNS, SNMP and new vectors.
  IoT device have the capacity to generate large traffic load
  Home and small office network now starting to have gigabit internet access speed, significantly impacting the capacity to create powerful attacks

## Slide 12: How can we protect IoT devices? -> Common sense
“Don’t even think of connecting an IoT device directly on the internet”
Always place IoT device behind a gateway / firewall
Don’t allow remote access to an IoT device
IoT Cloud
Services
x
x
x

## Slide 13: How can we protect IoT devices? -> Best practice & new standards
Rule #1: Identify IoT devices on your home network
Rule #2: Place a policy around the IoT device that restricts it to a specific function (default is no access)
Rule #3: Monitor for behavioural changes in the device and quarantine at the first sign of change.
Home Security
PDAP
Appliances
PDAP
Sensors
PDAP
Management
Application
IoT Cloud
Services
PDAP: Per Device Access Policy

## Slide 14: How do we provision new IoT devices? -> Application of emerging standards
The IETF is working on a Manufacturer Usage Description (MUD) specification to help with IoT device provisioning and automated network access control configuration.
  https://datatracker.ietf.org/doc/draft-ietf-opsawg-mud
I’m an ACME water sensor
- MUD File at: https://acme.corp/mud/ws1.0.json
MUD FILE:
- I have WIFI & apply the water sensor access policy
- I need to upgrade my firmware at https://acme.corp
- Configure me at https://myip/setup
- Alerts available at https://myip/alerts

## Slide 15: Manufacturer Usage Description (MUD) -> A unique device identifier (label)
The MUD file content would be available on the vendor’s web site (model type and firmware version)
  https://acme.corp/mud/water-sensor-1.0.json
The MUD file URL would be available on the IoT device as a QR code or as a network parameter
It would be nice if the IoT device could advertise it’s current firmware version and/or current MUD file URL via WIFI or network connection (DPP, DHCP, LLDP…) on order to setup correct security profile

## Slide 16: High Level MUD & IoT Device Provisioning Workflow
MUD Controller
(1)
Scan MUD
QR code &
send to MUD
controller
CIRA SHG
MUD Repository
SHG
App
(2)
Send to
CIRA
(2)
Get vendor
MUD file
ACME.CORP
MUD
Repository
SHG
ACME.CORP
IoT Water Sensor
(1)
(3)
User accepts
provisioning
instructions
MUD QR Code
(1)
(4)
IoT device added to network with specific network access controls
Network Access control:
Allow access to ACME.CORP
Allow to send alerts internally
Allow to be configured by app
Deny all other internet access
(4)
(IP Tables)
MUD Supervisor

## Slide 17: You guess it! That’s why we need a simple provisioning interface this stuff is complex!

## Slide 18: Removing End User Complexity -> Simple user interface
The previous slides have outlined the high level workflow. The actual workflow and automation can be very complex.
One key goal of this project is to present the users with very simple choices to provision and administer a potential complex network.
Ideally, the user can only swipe up, down, left and right.

## Slide 19: Quarantine of compromised devices -> Behavioural analysis
The policy part of the MUD profile is created to provide an additional level of protection for the network. This ensures the device will function only as intended and once behavioural changes are noted then the device is logically segregated from the network (quarantine)
Appliances
Management
Application
x
The refrigerator is quarantined
- Bad lettuce 

## Slide 20: Secure Remote Access -> Trusted authentication & accessible
Removing the complication surrounding enabling trusted secure remote access to home network is a key goal of this project (not for the initial prototype)
Need an internet resolvable domain name for the SHG to remotely connect. i.e. “myhome.ca”
Mobile
myhome.ca
The prototype will use securehomegateway.ca 3rd level domains

## Slide 21: The focus is on Automation
+
Secure Gateway
Provisioning Automation
Secure Device
Provisioning Automation
Innovation
Notes: http://www.istockphoto.com/ca/photo/home-network-gm117311543-7381629

## Slide 22: Step 1 (this is the revised story )
When you buy a CIRA secure home gateway, it comes bundled with a DNSSEC signed 3rd level .CA domain.
+
QR Code to activate provisioning and domain)
3rd level domain
domain.securehomegateway.ca
+

## Slide 23: Step 2 – SHG Setup
Follow the configuration instructions
  Install & open the CIRA SHG App
  Power on the SHG
  Scan the SHG QR code for initial setup
  System Assigned 3rd level domain name
  Setup split view Internet/External DNS for SHG domain
  Home Gateway ready for configuration
SHG
Application

## Slide 24: Step 3 – DNS Magic – Work in progress…
Automated DNS Backend Provisioning @ CIRA
  CIRA creates the 3rd level .CA SHG domain w/DNSSEC
  SHG and CIRA sync on external view propagation, internal SHG DS record synced in external DNS view. (full chain of trust internally and external on SHG domain)
  Need synchronisation between external SHG DNS record and SHG external IP address
SHG External
Domain Provisioning
& Primary DNS
External
DNS view
Hidden Primary
Internal
DNS view
Secondary DNS
D-Zone
? Which one is primary - WIP ?
SHG External
IP Address

## Slide 25: Step 4 – Current focus is on automated WIFI setup – that’s challenging!
Setup secure home network infrastructure
  Using your SHG App, scan the QR code of each new device to:
    Discover the MUD profile
    Transfer the unique WIFI credentials (per MAC address)
    Assign the appropriate Device Access Policy

## Slide 26: Simple user interface is key to this project: Swipe UP, DOWN, LEFT and RIGHT
Gateway provisioning, device discovery, device provisioning must be as simple as possible, intuitive for non experienced users, available as framework for default open source app.

## Slide 27: High Level Architecture (very ;-)
OpenWrt
Home Gateway
Home Network
CIRA SHG Registry
Internal DNS/DNSSEC
External IPSEC
D-Zone firewall
3rdlevel.securehomegateway.ca
Home Gateway
Provisioning
3rd Level .CA home domain
Primary DNS
D-Zone
IoT Cloud
Services
&
D-Zone Firewall
Secure Remote Home Network Access
Wifi MiFi Zigbee
NFC RFID

## Slide 28: We are building a Prototype -> Based on Omnia Turris Gateway
Develop a Proof of Concept and prototype
  Using .CZ Omnia Home Gateway & openWRT
  IoT device provisioning based on MUD
  Home Gateway App (Android/iPhone)
  Develop some IoT discoverable devices and MUD profiles
Use public GitHub to document the functional specification and repo for prototype software
  Functional specification (Work in progress)
  Open source software repository
  https://github.com/CIRALabs/Secure-IoT-Home-Gateway

## Slide 29: Specifications we are currently leveraging
Specifications we are leveraging:
https://datatracker.ietf.org/doc/draft-ietf-opsawg-mud/
https://datatracker.ietf.org/doc/draft-ietf-netmod-acl-model
RFC 7368
RFC 8375
https://datatracker.ietf.org/doc/draft-ietf-homenet-simple-naming
https://datatracker.ietf.org/doc/draft-ietf-homenet-front-end-naming-delegation
RFC 4033,4034,4035 (DNSSEC)
https://datatracker.ietf.org/doc/rfc5011/
RFC 4795
Specifications we are planning/considering:
RFC4301, RFC7296 (IPsec. Considering OpenVPN too)
RFC8366, https://datatracker.ietf.org/doc/draft-ietf-anima-bootstrapping-keyinfra/
https://datatracker.ietf.org/doc/draft-cheshire-dnssd-roadmap/
https://datatracker.ietf.org/doc/draft-ietf-dnssd-hybrid/
https://datatracker.ietf.org/doc/draft-cheshire-dnssd-roadmap/
https://datatracker.ietf.org/doc/draft-ietf-dnssd-mdns-relay/
Specifications we are writing:
- draft-richardson-opsawg-securehomegateway-mud-00
How we are using,extending, MUD.
- draft-richardson-anima-smartpledge-00
How we will leverage a DPP-like QR code to do initial enrollment of the *ROUTER*

## Slide 30: This slide deck is a vision it’s what we’ll be using In 5 years
Is work in progress, presented as a story
  Story how a home gateway can be user and IoT friendly
Is meant to define a security framework and associated standards
  IETF, ISO/IEC, others..
Is tuned around implementation at .CA / CIRA, but not specific just for CIRA
Is to solicit feedback
Is another layer of defence (in depth) to protect the internet against nasty (IoT) devices

## Slide 31: What do you think?
Project Information
https://github.com/CIRALabs/Secure-IoT-Home-Gateway
Prototype code
https://github.com/CIRALabs/

## Slide 32: Roadmap – Future functionality that has been proposed / identified
Next slides things we identified for potential future work or functionality
Includes ideas, comments & feedback

## Slide 33: IoT Service / action type -> Generic IoT home controller
Status: Up/down, on/off, ok/bad, status variable
Audio/Video: Camera, video feed
Media: Audio/Video media feed, TV, music
Storage: Data storage, NAS (pictures, files, data)
Alerts: Up/down, on/off, ok/bad, “Water detected”
Control: Turn up/down, on/off, change device value
Cloud Service: IoT vendor, Google, MS, DropBox
VPN (VPN inside vpn.myhouse.ca)
Remote house access
Quarantine, New MUD profile available
Other Sensors/ Actuator functions?

## Slide 34: Adding remote VPN access to trusted mobile and computers
Mobile
(1) Discovery services
(2) Grant permission and credentials to mobile for remote home access

## Slide 35: Adding your Car to remotely access your home network
Car
(1) Discovery services
Control car feature
Grant permission and credentials to car mobile for remote home access
View car alerts
View car status/location
(2) Assign roles

## Slide 36: Should the inside of your car should be part of your home network as well?
Notes: http://www.istockphoto.com/ca/photo/intelligent-vehicle-cockpit-and-wireless-communication-network-concept-gm692837788-127932641

## Slide 37: List of IoT scenarios to be assessed
Example of pushing WIFI to the device
Show that the fridge is exposing service
No web interface on IoT device
Focus on cloud / vendor, show they integrate into this solution, can be multi vendor multi cloud provides
IoT Classification: based on device type, air play could see all camera in the house, the TV could see all camera (security controls)
Door bell sends to audio device, you car
Fire alert send to audio receiving device
SmartGRID company allow access to home gateway
  allow SmartGRID to access hot water tank
  allow SmartGRID to adjust thermostats