## Slide 1: Secure IoT Home Gateway & Home Registry – Idea & vision Open standards development
Jacques Latour, CTO Canadian Internet Registration Authority January 24, 2018

## Slide 2: 2 distinct ideas into one solution
IoT Secure Home Gateway
.CA Home Registry
IDEA #1 – ccTLD Home Registry
Value Proposition:
For ccTLD, to have a domain per household
Leverage the DNSSEC chain of trust by having a registered domain for home use
IDEA #2 – Secure Gateway
Value Proposition:
To create a security framework to protect the Internet from IoT device attacks
To enhance the home network privacy & security with network access controls

## Slide 3: Secure Home Gateway & Registry Idea
For many internet organizations, the #1 risk on their risk register is a large scale (Dyn like) DDoS attack. One of the mitigation mechanisms for this risk is to prevent weaponization of IoT devices
Protecting IoT devices at the edge is another layer of security that should be further developed
The security controls would be aimed at protecting the IoT devices from the internet, and to protect the internet from IoT devices.

## Slide 4: IoT Threat landscape SPECIFIC TO THE INTERNET - CURRENT
IoT device compromises:
  Used in internet attacks i.e. MIRAI/DYN Attack (DDoS) targeting DNS servers (1.2 Tbs)
IoT traffic reflection and amplification
  IoT device used to amplification traffic attack (DDoS) NTP, DNS, SNMP.
DNS compromises
  Can be used to spoof DNS name, redirecting users to compromised web sites or services.
IoT devices must not have wide open internet access, inbound/outbound internet access must be controlled.

## Slide 5: Today’s Home Network & IoT implementation are disparate, kind of scary & IN need OF structure!
Notes: http://www.istockphoto.com/ca/photo/internet-of-things-concept-with-network-of-connected-objects-gm644680544-116869175

## Slide 6: The home network of the future must be safe, secure and simple to use!
Notes: http://www.istockphoto.com/ca/photo/circular-futuristic-interface-of-smart-home-automation-assistant-virtual-screen-gm637770524-113940363

## Slide 7: The home network must be reachable from the internet seamlessly and securely
Notes: http://www.istockphoto.com/ca/photo/businessman-touching-a-cloud-connected-to-objects-internet-of-things-gm514785054-88267551

## Slide 8: even your car WILL be connected to your home network
because your home is bigger than your house
Notes: http://www.istockphoto.com/ca/photo/intelligent-vehicle-cockpit-and-wireless-communication-network-concept-gm692837788-127932641

## Slide 9: The home network grows to include personal and wearable IoT, inside and outside the home…
because eventually they will be IPv6 enabled
Notes: http://www.istockphoto.com/ca/photo/man-wearing-vr-headset-gm583697902-99848893

## Slide 10: Your home network security both internal and external must be protected using a common key
Notes: http://www.istockphoto.com/ca/photo/smart-phone-remote-for-smart-home-hologram-technology-concept-gm839028202-137738281

## Slide 11: Leveraging the chain of trust in DNSSEC and some innovation to create a secure home network platform
Notes: http://www.istockphoto.com/ca/photo/digital-handshake-on-blue-background-gm613033814-105721913

## Slide 12: Do WE need to say more?
Public service announcement: We’re out of IPv4 addresses !!!
Notes: http://www.istockphoto.com/ca/photo/ipv6-new-internet-protocol-gm502837022-82158325

## Slide 13: what does this bring to the ccTLD domain industry?
A domain name per household!!!
myhome.ca
myhome.net.ca
IoT
Cloud
services
Notes: http://www.istockphoto.com/ca/photo/home-computer-network-gm98265636-7381753
Need new picture, looks ugly ;-)

## Slide 14: home.arpa. draft-ietf-homenet-dot-14
IETF working on making the default home network address: [yourprinter.]home.arpa.
<<The naming mechanism needs to function without configuration from the user. While it may be possible for a name to be delegated by an ISP, homenets must also function in the absence of such a delegation.>>
Let’s make delegated “home” domains function without user configuration!

## Slide 15: The focus is on AutomatioN
+
Registry
Automation
Home Network
Automation
Innovation
Notes: http://www.istockphoto.com/ca/photo/home-network-gm117311543-7381629

## Slide 16: Your local ccTLD will provision your DNSSEC signed domain internally on your gateway and externally as DNS primary, and establish a secure chain of trust to your home gateway, magically solving all your worries and keeping your online family safe 
Notes: http://www.istockphoto.com/ca/photo/young-girl-looking-up-at-a-stereoscopic-vision-of-the-earth-internet-of-things-gm690778240-127332717

## Slide 17: Remember, it’s an idea. So far it looks like this…
That’s
a napkin
design


## Slide 18: What about IoT security? What about the home network?
Protect IoT device (inbound and outbound access)
Rule 1: Place behind firewall
Rule 2: Segment network by IoT type (NAC)
Rule 3: Control access to and from the IoT device
Home Security
Multimedia
Appliance
Sensors
Management
IoT Cloud
Services

## Slide 19: Network Access control (NAC) & default security controls
Something like ; packetfence on openwrt
Example of default zone security controls / policies
  Home Security -> may have access to cloud
    Emergency services may have access
  Sensors -> no access to internet
    Apppliances may have access this zone
  Appliance -> no access to internet
    VPN may have access this zone
  Allow myhome.ca to access myparents.ca
    Only for Home Security and sensors

## Slide 20: Step 1
When you buy a home gateway, it comes bundled with a .CA home network domain
+
RFID card
(Code to activate provisioning and domain)
A 2nd or 3rd level domain
i.e. myhome.net.ca
i.e. myhome.ca

## Slide 21: Step 2
Then you follow the provisioning instructions
  Install & open the CIRA Home Gateway app
  Turn on the Home Gateway
  “TAP” your mobile to discover the home gateway
  Pick a domain name, 2nd or 3rd level domain name
  Enter the secret code (“TAP” RFID card)
  Home Gateway ready for configuration
myhome.ca code
+

## Slide 22: Step 3
Automated Backend Provisioning @ CIRA
  CIRA creates the .CA domain name in the registry
  CIRA signs the .CA domain with DNSSEC
  CIRA is primary for the external DNS view of the .CA domain
  CIRA provides secondary DNS to the .CA domain
+
+
DNSSEC
(Keys)
EXTERNAL
(Internet)
.CA
Registry

## Slide 23: Step 4 (NEEDs WORK)
Automated Home Gateway provisioning
  Establish secure connection to Home Gateway
  Securely send private DNSSEC key to Home Gateway, setup internal DNS and DNSSEC
  Configure Home Gateway for DNS integration with registry (à la dynamic DNS) for external services
+
DNSSEC
(Keys)
EXTERNAL
(Internet)

+
INTERNAL
(Home Network)
Dynamic DNS

## Slide 24: Step 5
Setup secure home network infrastructure
  Using your trusted mobile & the app, “TAP” the Home Gateway to:
    Learn the WIFI password
    Get the IPSec password, SSO tokens and keys to VPN in your home network
  Use your mobile and “TAP” all your IoT devices to add on your home WIFI network, easy peasy 

## Slide 25: At this point we have
A home gateway fully provisioned with a .CA domain name, with both internal and external domain name resolution, signed with DNSSEC.
  WIFI and other networks securely provisioned and setup
Now we’re ready to provision the IoT devices
Internal domain fully operational
Secured internally by DNSSEC
External domain to allow exposing internal services and make them available externally
fridge.la-house-a-latour.ca Internal IP
printer.la-house-a-latour.ca Internal IP
vpn.la-house-a-latour.ca External IP

## Slide 26: Now, let’s see how we provision IoT DEVICES IN HOME NETWORK
Once the IoT device has network access TAP to discover
IoT device exposes via RFID (or similar) the services available
Pick relevant IoT services category fro provisioning
Expose Services
JSON blob / RFID

## Slide 27: adding remote vpn access to trusted mobile
Mobile
(1) Tap the mobile
Discover services
(2) Grant permission and credentials to mobile for remote home access

## Slide 28: Adding your Car to remote access your home network
Car
(1) Tap the car
Discover services
Control car feature
Grant permission and credentials to car mobile for remote home access
View car alerts
View car status/location
(2) Assign roles

## Slide 29: IoT Service / action type
Status: Up/down, on/off, ok/bad, status variable
Audio/Video: Camera, video feed
Media: Audio/Video media feed, TV, music
Storage: Data storage, NAS (pictures, files, data)
Alerts: Up/down, on/off, ok/bad, “Water detected”
Control: Turn up/down, on/off, change device value
Cloud Service: IoT vendor, Google, MS, DropBox
VPN (VPN inside myhouse.ca)
Remote house access
Other Sensors/ Actuator functions?

## Slide 30: TODO: Scenario: Adding a smart TV
WORK IN PROGRESS

## Slide 31: TODO: + ADD Scenarios FOR each device type
TODO: as part of the functional specification documentation.
Example of pushing WIFI to the device
show that the fridge is exposing service
And ready to receive services {WIFI}
No web interface on IoT device
Focus on cloud / vendor, show they integrate into this solution, can be multi vendor multi cloud provides

## Slide 32: Your home network security is compromised?
Get the ccTLD to perform an emergency DNSSEC key roll over, externally and on the home gateway
Will have new keys on home gateway
This will make all VPN keys & certificate invalid
A roll over will force the generation of new keys.
  Trusted “management” home gateway mobile access must be re-established using an out of band token
  Remote home access trust must be re-established
  Local network access controls should remain the same

## Slide 33: High Level SOLUTION Architecture
OpenWrt
Home Gateway
Internet Home Network Trust
Home Network Registry
Internal DNS/DNSSEC
External IPSEC
D-Zone firewall
myhome.ca
Home Gateway
Provisioning
.CA home domain
Primary DNS
.CA home domain
IPv6 ONLY

IoT Cloud
Services
(D-Zone Firewall)
Remote Home Network Access
(VPN IPSec)
Wifi MiFi Zigbee
NFC RFID

## Slide 34: What do you think?
Want to help?

## Slide 35: Going forward, it’s a journey! ccTLD Value proposition
Motivation
  Ensure long term ccTLD relevance in the future of IoT
  To create a secure <internet home> IoT environment
Proposing ccTLD to develop a solution
  To keep the home network safe and secure
  To leverage DNSSEC as an innovation platform to create a hub for “home trust”
  That leverages the ccTLD registry expertise
  To enhance OpenWRT with this functionality

## Slide 36: Next Steps – build a PRototype
Develop a Proof of Concept and prototype
  Using .CZ Omnia Home Gateway (openWRT)
  Home Gateway App (Android/iPhone)
  Develop some IoT discoverable devices (RFID)
Use public GitHub to document the functional specification and repo for prototype software
  Functional specification
  Software repository

## Slide 37: This slide deck is a vision it’s what we’ll be using In 5 years
Is work in progress, presented as a story
  Story how a home gateway can be IoT friendly and how a ccTLD registry provision a secure domain per household
Is meant to define a security framework and associated standards
  IETF, ISO/IEC, others..
Is tuned around implementation at .CA / CIRA, but not specific just for CIRA
Is to solicit feedback
Is another layer of defence in depth to protect the internet

## Slide 38
The new <Internet Home>
https://github.com/CIRALabs/Home-Network-Registry-Gateway